## Slide 1: Agriculture in GAINS Focus on ammonia emissions and mitigation opportunities
Zbigniew Klimont (klimont@iiasa.ac.at)

## Slide 2: Source apportionment of PM2.5 in Delhi 2015
Amann et al., 2017; Atmospheric Environment

## Slide 3: Origin of PM2.5 - 2009
Source: IIASA GAINS
Netherlands average of the urban AIRBASE stations
Lyon, Centre Ville

## Slide 4: Key sources of ammonia emissions in the various steps of the livestock production and animal manure management chains Source: TSAP report #3

## Slide 5: NH3 emissions from livestock farming, by emission stage
Source: IIASA GAINS

## Slide 6: NH3: Key measures for achieving the proposed NECs
Improved storage of manure (e.g., closed tanks) at large farms
Improved application of manure on soil, e.g., trailing hose, slot injection (for large farms)
Improved application of urea fertilizer or substitution by ammonium nitrate

## Slide 7
Improve application of manures on soil, e.g., trailing hose, slot injection
There are proven ways of better managing the manure ‘resource’ – it will reduce demand for mineral fertilizer too
Improved storage of manures, e.g., closed tanks, anaerobic digestion

## Slide 8: 80% of NH3 emissions emerge from 5% of the farms in the EU Zero LSU (livestock units) refers to arable farms without animals
NH3 emissions # of farms
Farm sizes:
Source: IIASA-GAINS

## Slide 9: Distribution of farm sizes – 2010 (only holdings with animals) Source: EUROSTAT

## Slide 10: NH3 emissions from livestock farming by farm size
Source: IIASA-GAINS, based on EUROSTAT

## Slide 11: Farm sizes have changed rapidly in the past – Prospects for 2030 not included in TSAP analysis
In Switzerland, continuation of the trend towards larger farms – assuming CLE legislation - would lead to 5% lower NH3 emissions in 2030

## Slide 12: Agriculture in GAINS
Principles of emission and cost calculation

## Slide 13: Key sources of ammonia emissions in the various steps of the livestock production and animal manure management chains Source: TSAP report #3

## Slide 14: GAINS - Agricultural module
Emission
factor
Livestock
(base year
and
forecasts)
Fertilizers
(base year, forecasts)
Housing period
Volatilization
rate, etc.
% N loss
Control
strategies
Emissions
and
Costs
Excretion rate
and volume
Current
practice
Legend:
- Data asked for and statistics
- Data available from guidebooks
- Data assumed in the model but available for review
- Result of calculation
Manure
system
Abatement
technologies
(efficiency, costs, etc.)
Other activities
(base year, forecasts)
Emission
factor
Climatic zone
Soil type
Farm size
Storage time
Other

## Slide 15: Emission calculation
where:
ELi,l ammonia emissions from livestock farming in country (i) and year (l) [kt NH3/year],
i,j,k,l country, livestock category, abatement technique, year;
s emission stage (four stages)
L animal population [thousand heads];
ef emission factor [kg NH3 / animal per year];
 reduction efficiency of abatement technique;
X implementation rate of the abatement technique
Source: Klimont and Winiwarter (2011)

## Slide 16: Emission factors at each stage are influenced by the nitrogen losses at previous stages
ef1 = Nx1 v1 (2a)
ef2 = Nx1 (1 – v1) v2 (2b)
ef3 = Nx1 (1 – v1 – (1 – v1) v2) v3 (2c)
ef4 = Nx4 v4 (2d)
where:
ef1,2,3,4 NH3-nitrogen loss at distinguished emission stages, i.e., housing (1), storage (2),
application (3), and grazing (4),
Nx1,4 N excretion during housing (1) and grazing (4),
v1,2,3,4 N volatilization rates at distinguished emission stages
Source: Klimont and Winiwarter (2011)

## Slide 17: Key categories of emission sources
  Animal categories (by housing type)
    Dairy cows, Other cattle, Pigs, Laying hens, Other poultry, Sheep and goats, Fur animals, Horses, Buffaloes, Camels
  N-Fertilizer application (urea and other fertilizers)
  Fertilizer production
  Stationary combustion
  Transport
  Open burning of agricultural waste
  Other

## Slide 18: Ammonia emission factors uncontrolled/reference system
Emission stage specific (livestock), estimated from national parameters (can change over time):
  N excretion,
  N volatilization rate,
  Production efficiency (e.g., milk production),
  Housing period,
  Climatic conditions,
  Soil type,
  Other…

## Slide 19
Categories of emission control options
Low nitrogen feed
Low emission housing
Air purification
Covered storage (low and high efficiency)
Low ammonia application (low and high efficiency)
Improved application or substitution of urea fertilizer
Incineration of poultry manures
Combinations of the above options
+ options to control non-CO2 GHG (CH4, N2O)

## Slide 20: Multi-pollutant measures (interactions); examples*) expected emission reduction (↓), potential increase (↑)
Agricultural sources:
  Low emission pig housing – NH3, CH4 ↓ N2O ↑
  Covered storage of slurry – NH3, N2O ↓ CH4 ↓↑
  Covered storage of FYM – NH3, N2O, CH4 ↓
  Storage, solids separation – CH4 ↓, NH3 ↑↓
  Injection/incorporation of manures – NH3 ↓ N2O ↑
  Anaerobic digestion (biogas) – CH4, CO2, N2O ↓ NH3 ↓↑
  Slurry acidification – NH3, CH4 ↓
  Open burning of agricultural residues – VOC, PM, CO, NH3, CH4 ↓
  Variable Rate Technology (fertilizer application) – N2O, NH3, CO2 ↓
  Cattle and sheep breeding (genetic selection) – CH4, NH3 ↓
*) Extensive discussion of several measures available in Sommer et al. (2013)

## Slide 21
Example of emission control options and their default removal efficiencies

## Slide 22: Examples of applicability rates [% of livestock]
Country/animal/technology | Low N feed | Low emission housing | Covered storage (high) | Low NH3 application (high)
Norway |  |  |  | 
Pigs (slurry/straw) | 100/100 | 0/0 | 15/0 | 0/0
Dairy cattle (slurry/straw) | 0/0 | 100/0 | 15/0 | 50/25
United Kingdom |  |  |  | 
Pigs (slurry/straw) | 100/100 | 60/0 | 15/0 | 35/100
Dairy cattle (slurry/straw) | 0/0 | 68/0 | 21/0 | 29/100
Hungary |  |  |  | 
Pigs (slurry/straw) | 100/100 | 100/0 | 0/0 | 60/100
Dairy cattle (slurry/straw) | 0/0 | 23/0 | 30/0 | 57/100
Switzerland |  |  |  | 
Pigs (slurry/straw) | 100/100 | 48/0 | 35/0 | 6/80
Dairy cattle (slurry/straw) | 100/100 | 43/0 | 20/0 | 6/80

## Slide 23: Cost categories distinguished in GAINS
Investments (function of the average farm size) I = cf+cv/ss or I = (cf*st*mp/ar2) + cv/(ss*ar) where: cf, cv - investment function coefficients ss, ar - average farm size, animal rounds per year, st, mp - storage time, manure “production”
Fixed operating costs: OMfix= I*fk
  fixed percentage (fk) of investments, includes: maintenance, insurance, administrative overhead;
Variable operating costs (OMvar) e.g., increase in feed price, energy, water and labour use, costs of waste disposal

## Slide 24: Investment cost
cif, civ – investment function coefficients
ss – average farm size
i,k,l – livestock category, abatement technique, country
or for storage
st – storage time
mp – manure ‘production’ per year
ar – production cycles per year
Source: Klimont and Winiwarter (2011)

## Slide 25: Annualized investments
i,k,l – livestock category, abatement technique, country
lt – lifetime of abatement technique
q – interest rate (4%)

## Slide 26: Examples of investment functions (storage of cattle manure)
Poland
UK

## Slide 27: Operating costs
fk – percentage of investment costs
Q – quantity of p
c – unit price of a given p
p – parameter type (additional energy, labour, waste disposal, etc.)
Source: Klimont and Winiwarter (2011)

## Slide 28: Costs of low ammonia application options
Cm – Cost of option k per m3
cif, civ – cost coefficients for a specific option k
Qmh – manure application rate for option k
i,k,l – livestock category, abatement technique, country
Sm – share of option k
Source: Klimont and Winiwarter (2011)

## Slide 29: Unit costs
efi,l – emission factor for livestock category i and country l
ŋk – removal efficiency of option k
ca – unit costs per animal-place
ar – production cycles per year
sb – capacity utilization factor
ŋk – removal efficiency of option k
Cost efficiency can be evaluated if the annual costs are related to the abated emissions

## Slide 30: Marginal cost
cnk – unit costs for option k
ŋk – removal efficiency of option k

## Slide 31: Example of a cost curve
+Air purification
+Housing
Storage and application
Urea subs.

## Slide 32: Costs differ by country
Agricultural practice
Implementation of measures
Farm size
Climate
Internal cost structure (labour cost, …)
 GAINS needs input!
Notes: 32

## Slide 33: GAINS unit costs ranges (1)
High efficiency
Low to medium efficiency
Dairy cattle
Other cattle
Notes: 33

## Slide 34: Some problems and uncertainties (NH3)
Issues with statistical data; inconsistencies between national and international data
Lack of local information about feed, efficiency, measurements of emission rates
Poor information on housing systems in place and their future evolution
Contradictory information on how existing legislation is or will be implemented
Emissions from non-agricultural sources often not reported
Better information on current practices could lead to significant improvements, i.e., development of regional emission factors

## Slide 35: Example of European cost data in GAINS (1)
Abatement option | Application area | Investments [€/animal-place] |  | Total costs* [€/animal/year] | 
 |  | Farm size ** |  |  | 
 |  | Small | Typical | Small | Typical
Low nitrogen feed | Dairy cows | n.a. |  | 45 | 
 | Pigs | 2.7 |  | 8 | 
 | Laying hens | n.a. |  | 0.1 | 
 | Other poultry | n.a. |  | 0.12 | 
Bio-filtration and | Pigs | 200-300 | 170 | 50-70 | 38-40
bio-scrubbers | Laying hens | 4.7 |  | 1.5-2.0 | 
 | Other poultry | 4.7 |  | 2.0-2.5 | 
Housing adaptation | Dairy cows, Other cattle | 450-550 | 400 | 90-110 | 75-90
 | Pigs | 90-94 | 89 | 21 | 19
 | Laying hens | 0.8 |  | 0.2-0.25 | 
 | Other poultry | 1.8 |  | 0.28 | 
Stripping/adsorption | Industry | 625 €/t NH3 removed |  |  | 
n.a.: not applicable
* - Taking into account fixed and variable operating costs
** - The following stable sizes are assumed:
Pigs - small (<50 animals/farm), typical (~170)
Dairy cows - small (<20 animals/farm), typical (~35)
Other cattle - small (<30 animals/farm), typical (~40)

## Slide 36: Example of European cost data in GAINS (2)
n.a.: not applicable
* - Taking into account fixed and variable operating costs
** - The following stable sizes are assumed: Pigs - small (<50 animals/farm), typical (~170);
Dairy cows - small (<20 animals/farm), typical (~35); Other cattle- small (<30 animals/farm), typical (~40)
Abatement option | Application area | Investments [ECU/animal-place] |  | Total costs* [ECU/animal/year] | 
 |  | Farm size ** |  |  | 
 |  | small | typical | small | typical
Covered storage - | Dairy cows | 200-400 | 160 | 40-60 | 18-40
high efficiency | Other cattle | 100-150 | 70 | 15-25 | 7-12
 | Pigs | 2-5 | 1 | 0.4-1 | 0.3
 | Laying hens | 0.4 |  | 0.06 | 
Covered storage - | Dairy cows | 100-200 | 80 | 20-30 | 9-20
low efficiency | Other cattle | 50-75 | 35 | 7-13 | 3-6
 | Pigs | 1-3 | 0.5 | 0.2-0.5 | 0.15
 | Laying hens | 0.2 |  | 0.03 | 
Low NH3 application | Dairy cows | n.a. |  | 50-70 | 
 | Other cattle | n.a. |  | 18-40 | 
 | Pigs | n.a. |  | 5-8 | 
 | Laying hens | n.a. |  | 0.15-0.3 | 
 | Other poultry | n.a. |  | 0.04-0.06 | 
 | Sheep | n.a. |  | 3-4 | 

## Slide 37: Further reading
IIASA reports produced in support of the EU Commission during its review of the Thematic Strategy on Air Pollution (TSAP)
http://www.iiasa.ac.at/web/home/research/researchPrograms/MitigationofAirPollutionandGreenhousegases/TSAP-reports.html
Kuczynski et al [eds] 2005. Emissions from European Agriculture, Wageningen Academic Publishers, Wageningen, the Netherlands
M. Sutton, S. Reis and S.M.H. Baker [eds] 2009. Atmospheric Ammonia. Springer
Bittman S., Dedina M., Howard C., Oenema O., Sutton M.A. [eds] 2014. Options for ammonia mitigation: Guidance from the UNECE Task Force on Reactive Nitrogen. Centre for Ecology and Hydrology, Edinburgh, UK.
Reis S., Howard C., Sutton M.A. [eds] 2015. Costs of Ammonia Abatement and the Climate Co-Benefits, Springer Netherlands