## Slide 1: GAINS cost-effectiveness analysis
Fabian Wagner
fabian@iiasa.ac.at
SPIPA GAINS Training, 12-16 April 2021

## Slide 2: Uses of the GAINS model
Activity-based emissions inventory (AP/GHG)
Simulation of future scenarios/incl. What if policies were implemented? (AP/GHG)
Comparison of alternative scenarios (AP/GHG)
Co-benefit analysis (GHG+AP)
Cost-effectiveness analysis (AP/GHG)
  Incl. cost curves

## Slide 3: Agenda
Why cost-effectiveness analysis
Optimization/GAINS cost concept/marginal costs
Target setting: recent examples from South Asia
The cycle of policy support and analysis
Conclusion

## Slide 4: Why cost-effectiveness analysis

## Slide 5: Integrated Assessment Model
A tool that provides useful information and facilitates decisions
Here: Provide answers to the
Central question for policy makers:
To what level should the emissions of air pollutants be reduced in some future year 20XX?
Where will emissions and effects be in year 20XX just with current policies in place?
What further reductions are technically feasible?
How much do they cost? – optimal/non-optimal
Who should take action?
Who (which countries/regions/sectors) pays?
How much are they willing to pay?
Who benefits?
Is it enough?
Is it fair?
Notes: Need the ability to analyze alternative futures (scenarios)

## Slide 6: Separate two questions?
Cost-effective solution?
Who is going to pay for it?

## Slide 7: Greenhouse gas–Air pollution Interactions and Synergies: The GAINS tool
National emission ceilings
National Emission Ceilings
Policy targets
Social development and economic activities
Emissions
Emission control options: ~2000 measures, co-control of 10 air pollutants and 6 GHGs)
Atmospheric dispersion
Costs
Health, ecosystems and climate impact indicators
Optimization

## Slide 8: Optimization: a primer
Linear optimization of air pollution control strategies in GAINS:
Objective: minimize (Costs)
s.t. EnvEffectk < Limitk
Minimize costs, such that environmental effects do not exceed pre-defined limits
(there are additional technology constraints, e.g.
  maximum application rates
  vintage structure
  etc)

## Slide 9: Cost concept used
All costs are in (economic) real terms (2015)
Societal costs:
  Standard discount rate: 4 percent p.a.
  Taxes not included
  Transaction & training costs not included
Feedback on economy not included (small)
Technology costs
  Non-technical measures not included
  Investment, Operating and Maintenance costs, Labour cost, Energy costs, etc.
  Are constant over time

## Slide 10: Cost information in the literature Example: Flue gas desulphurization (FGD)
Scrubber type | Unit size MW | Capital Cost $/kW | O&M cost - fix $/kW | O&M cost - var $/MWh
Wet | >400 | 100-250 | 2-8 | 0.5-2
Wet | <400 | 250-1500 | 8-20 | 0.5-2
Spray dry | >400 | 40-150 | 4-10 | 0.5-2
Spray dry | <400 | 150-1500 | 10-300 | 0.5-2
Cost components

## Slide 11: Annualizing investment costs
q = discount (interest) rate , n = lifetime of installation

## Slide 12: Units used
Costs per unit of activity
  E.g. MEuro per PJ
Costs per ton of pollutant removed
  E.g. Euro per ton of SO2
“per year” is always implicit

## Slide 13: Costs are country- and technology-specific
Technology-specific factors:
Investments, fixed O+M
Demand for labour, energy, by-products
Lifetime of equipment
Removal efficiency
Country-specific factors:
Installation size, plant factors
Prices for labour, energy, by-products, etc.
Applicability

## Slide 14: Cost calculation methodology
Costs per activity unit:
Ian | Annualised investments
OMfix | Fixed operating & maintenance costs
OMvar | Variable operating & maintenance costs
pf | Capacity utilisation
Costs per emission removed:
ef | Uncontrolled emission factor
η | Removal efficiency

## Slide 15: Unit costs: per fuel vs per tSO2 reduced
 | Emission factor ktSO2 /PJ | Unit cost/ PJ | unit cost/ tSO2
no Control | 2.000 |  | 
LINJ | 0.750 | 0.6 | 0.48
PWFGD | 0.100 | 0.4 | 0.21
RFGD | 0.050 | 0.7 | 0.36

## Slide 16: Unit costs vs marginal costs graphically
No control
PWFGD
RFGD
PWFGD
RFGD

## Slide 17: Unit costs vs marginal costs
MC12= -(UC2 – UC1)/(∆E2 - ∆E1)
UCi : unit cost technology i [EUR/PJ]
∆Ei: emissions reduced relative to no-control, e.g. [t/PJ]
Example:
Marginal cost for using technology 2 when technology 1 is in place:

## Slide 18: Cost-effectiveness analysis: How do we reduce pollution in the most cost-effective way?
Marginal abatement cost curves are part of the answer, but not all of it!

## Slide 19: The GAINS optimization is formulated as a linear programming (LP) problem
What are the decision variables? What choices does the GAINS have in the optimization?

## Slide 20: Revisiting the emissions calculation
E.g. power plants
Emissions = (activity data) x (emission factor)
Coal (HC3) use
We can do this for every sector-activity-pollutant combination!

## Slide 21: Technology specific activity data
Emissions = (activity data) x (emission factor)

## Slide 22: Technology-specific activity data
Variables in the optimization = (activity data) x (control strategy)

## Slide 23: The GAINS optimization is formulated as a linear programming (LP) problem
i emission region
s GAINS sector
f GAINS fuel/activity
t GAINS technology

## Slide 24: Types of constraints
Environmental/Impact targets
Generic technology constraints
  Maximum application rates/shares not suitable for controls
  Vintage structure
  Fixed application rates
Average emission factors (per sector/activity) can only decrease, not increase. [Emission standards can only become stricter]

## Slide 25: Setting targets
impact indicator
Option 1: Air quality target in every grid cell
Impact indicator: concentration
k: each grid cell
(approx. 6,500 inequalities)
Option 2: Gap closure on concentration in every grid cell
Impact indicator: concentration
k: each grid cell
(approx. 6,500 inequalities)
Option 3: Gap closure on total mortality
Impact indicator: mortality
k: only one EU aggregate
(1 inequality)

## Slide 26: Greenhouse gas–Air pollution Interactions and Synergies: The GAINS tool
Policy targets
Social development and economic activities
Emissions
Emission control options: ~2000 measures, co-control of 10 air pollutants and 6 GHGs)
Atmospheric dispersion
Costs
Health, ecosystems and climate impact indicators
Optimization

## Slide 27: Narrative: AQ outlook to 2030 – airshed management will be important
Potential impacts of recent policies in 2030
  for different assumptions on the implementation effectiveness
Scope for further measures: with all additional measures in GAINS
  showing potentials for improvements from domestic measures and for spillovers from other regions
Four options for next steps:
  Popular additional measures
    Region-wide application of a common set of popular measures
  Most effective low-cost measures in each region
    A uniform limit on marginal costs for improvement of the domestic exposures in all regions
    Ignoring spillover benefits to other regions, thus not really cost-effective
  Bring pop-weighted exposure below WHO IT1 (35µg.m-³)
    Cost-effectiveness optimization, explore distributional issues
    Demonstrate the need for an airshed approach across IGP
  90% towards WHO IT1 in all regions
Explore distributional issues; implications for airshed strategies

## Slide 28: India: Impact of recent policies in 2030
Contributions from natural sources

## Slide 29: Cost-effectiveness analysis: How do we reduce pollution in the most cost-effective way?
Marginal abatement cost curves are part of the answer, but not all of it!

## Slide 30: Scope for additional measures in 2030
Contributions from natural sources

## Slide 31: Option 1: ‘Popular additional measures’
A common set of popular measures applied throughout SAR
Based on government announcements
Considering gradual phase-in

## Slide 32: Option 1: Popular additional measures

## Slide 33: Option 2: Most effective low-cost measures in each region
Based on region-specific cost curves for exposure reductions to PM2.5
In each region, all measures with marginal costs below 80 million Euro/µg.m-3 are selected
However, these cost curves consider only exposure reductions within the same region, and do not include spill-overs to other regions. Total exposure reductions (incl. impacts on other regions) could be twice as high.
Bihar Delhi NCT

## Slide 34: Option 2: Most effective low-cost measures in each region

## Slide 35: Option 3: Bring pop-weighted exposure in all regions below WHO IT1 (35µg.m-³)
This does not address hot-spots where local measures will be most effective
Allowing measures that are required/cost-effective for achieving the targets in other regions
This target requires action mainly in the IGP, Bangladesh and Pakistan, while in other areas it will be attained already by full application of current policies
Distribution of costs – largest efforts with excessive costs in regions with highest concentrations, even if a large share originates from natural sources

## Slide 36: Option 3: Bring pop-weighted exposure in all regions below WHO IT1

## Slide 37: Option 4: 90% towards WHO IT1 in all regions
Target: Reduce current (here: 2030 baseline) exceedance of WHO IT1 by 90% in all regions
  A cooperative approach, all regions take the cost-effective measures to enable a 90% reduction of WHO IT1 excess throughout SAR
  Some IGP States overachieve the 90% reduction due to the need to achieve target in Delhi

## Slide 38: Option 4: Reduce 2030 exceedance of WHO IT1 by 90% in all regions

## Slide 39: Exposure reductions vs costs

## Slide 40: Distribution of costs in 2030 (% of GDP)

## Slide 41: Emission reductions: 90% to WHO-IT1 vs Low-cost scenario
Effective low-cost measures 90% towards WHO IT1

## Slide 43: The iterative process: 11 GAINS reports supporting the EU Thematic strategy on Air Pollution
1
2
3
4
7
5
6
8
9
10
11
Report on Current Legislation Emissions
Report on causes for recent emission reductions
Report on Agriculture
Report on Mobile Source
Report on Households
June 2012
February 2014
Report on Health end Environmental Impacts
Report on Scenarios for cost-effective controls
Report on Compliance with EU Air quality
Report on modeling compliance in GAINS
Report on policy scenarios
Report on final policy scenarios

## Slide 44: The iterative process: 5 additional GAINS reports supporting the EU Thematic strategy on Air Pollution
11
Report on final policy scenarios
February 2014
January 2015
12
13
Report on resulting urban air quality
Report on bilateral consultations
14
Report on updates in the input data
15
Report on a flexibility mechanism
16
Report on adjusted historic emission data

## Slide 45: Conclusions

## Slide 46: Conclusions
Cost-effective solutions typically save money vis-à-vis other approaches
Optimization techniques can help to identify such solutions
The GAINS cost-effectiveness analysis has been used in many regions of the world to guide policy makers
It is useful to separate the goal of overall cost-effectiveness from questions of distribution
The choice of environmental/health impact targets – type and ambition level – is a political one. (Cost-effective) scenario analysis can reveal advantages and disadvantages of the options.