## Slide 1: Calculating ambient PM2.5 and health impacts in GAINS
Gregor Kiesewetter
Pollution Management Group
Energy, Climate and Environment Program
IIASA
Laxenburg, Austria
GAINS training workshop, April 2021

## Slide 2: Overview
Introduction: Principles of source-receptor calculations
Health impact calculations
GAINS-South Asia – current implementation, plans

## Slide 3: The GAINS model
activities
Emission factors
emissions
Dispersion,
atmospheric chemistry
Control technologies
PM2.5 exposure
Health impacts
Mitigation strategies
Cost optimization
Dose-response
costs
unit costs
targets
Today

## Slide 4: Principles: PM2.5
PM2.5 is composed of primary PM and secondary aerosols
  PPM dispersion
  SO2
  NOx SIA formation: (NH4)2SO4 , (NH4)NO3
  NH3
  VOC SOA formation
  Natural dust, sea salt
  → Pure dispersion models (e.g. Aermod) are not enough, but can be useful at local scale
State of the art atmospheric chemistry-transport models (CTMs) can describe ambient PM2.5 concentrations well, but are time consuming:
  Emission gridding needed every time
  Execution time of the CTM – typically days per 1 year simulation with good resolution
Needed: fast approximation of the full atmospheric model with similar performance
GAINS approach: linearized response model (“atmospheric transfer coefficients”) derived from sensitivity simulations of a full CTM.
Total PM2.5

## Slide 5: Natural and anthropogenic contributions to PM2.5 in ambient air - 2018
Source: IIASA GAINS
Total PM2.5 concentrations
From natural sources (soil dust, sea salt)
From anthropogenic sources

## Slide 6: Composition of ambient PM2.5: Primary and secondary PM2.5
PM2.5 from primary PM emissions from anthropogenic sources | 
Source: IIASA GAINS
Secondary PM2.5 formed from SO2, NOx, NH3 and VOC emissions

## Slide 7: 0.5° transfer coefficients
We use sensitivity simulations of EMEP CTM on 0.5° to derive transfer coefficients country (region) → grid . Each sensitivity run changes emissions of pollutant from region by 15%:
For each source region and 5 source pollutants: PPM2.5, SO2, NOx, NH3, VOC
1 additional simulation reducing low-level PPM sources
Source region r
Receptor grid i
Pollutant p

## Slide 8: Transfer coefficients
Linear approximation of the full CTM
… 0.5° grid cell
… source pollutant (PPM2.5, NOx, SO2, NH3, VOC)
r… source region
… transfer coefficient from emissions of pollutant in region to grid cell
… emissions of pollutant in region
… grid specific constant: natural sources, boundary conditions, non-linearities
(PPM is actually split into high stack and low-level to take into account the different dispersion characteristics!)

## Slide 9: Example: 0.5° atmospheric transfer coefficients
Transfer coefficients represent the change in ambient PM2.5 if 1 kiloton more is emitted!

## Slide 10: Downscaling for urban areas
0.5° resolution ~ 50km. Not sufficient for urban concentration variation!
Mostly primary PM emissions from low-level sources are responsible for small scale variations (urban increments) in ambient PM concentrations!
  Relevant sectors:
    Residential combustion
    Road traffic
    Municipal waste burning
GAINS splits these sectors into urban and rural (traffic only internally)
Special sensitivity simulations were done with higher resolution (0.1° / 10km) changing only low-level urban emissions
  Split of the PPM low-level transfer coefficient into urban and rural

## Slide 11: Comparison of monitoring data with model estimates
Alternative metrics for different purposes: | 
Peak concentrations: for compliance with ambient air quality standards | Grid-average concentrations: a spatially more representative measure
Concentrations at specific monitoring sites: for validation of model results | 
Observed PM2.5 in Delhi - 2018
Population- weighted mean exposure in Delhi
Alternative metrics for different purposes: | 
Peak concentrations: for compliance with ambient air quality standards | Grid-average concentrations: a spatially more representative measure
Concentrations at specific monitoring sites: for validation of model results | Population-weighted mean exposure: to maximize economic efficiency of AQM strategies
Modelled grid-average PM2.5 in Delhi - 2018
GAINS calculates ~10 km*10 km
grid average concentrations
Modelled grid-average vs. observed PM2.5 in Delhi - 2018

## Slide 12: PM2.5 and human health
Long-time exposure to PM2.5 increases the risk of cardiovascular and respiratory diseases, and lung cancer
3-5 million cases of premature deaths annually are attributed to it,
making it the most important environmental risk factor for human health.

## Slide 13: Health impact calculations in GAINS
Outside Europe, GAINS follows the approach of the Global Burden of Disease studies
We calculate disease and age specific mortality
Long-term exposure increases the risk for death from a few diseases: COPD, stroke, IHD, lung cancer, ALRI.
Needed:
  Ambient PM2.5 concentration on relevant resolution (urban background)
  Population data on the same spatial distribution
  Exposure-response relationships
  Baseline mortality data (by disease and age)
GAINS
worldpop.org.uk (100m grid)
International literature: GBD, WHO,…
UN World Population Prospects (total mortality)
GBD (disease contributions)

## Slide 14: Population attributable fraction
PAF is the proportional reduction in population disease or mortality that would occur if exposure to a risk factor were reduced to an alternative ideal exposure scenario (eg. no air pollution).
... Disease (COPD, IHD, Stroke, lung cancer, ALRI)
… age
… level of PM2.5 concentrations
… fraction of the population exposed to PM2.5 of level
…Relative risk from disease at PM2.5 level for people at age
Attributable number of deaths:
: deaths attributable to PM2.5 (“premature deaths”) at age from disease
: baseline (=total) deaths at age from disease

## Slide 15: Integrated exposure-response functions
Many versions have been developed. Currently GAINS uses those from WHO 2016 / GBD 2013.
ALRI
COPD
Lung cancer
IHD
Stroke

## Slide 16: What GAINS currently calculates
Ambient PM2.5 concentration maps
Population-weighted mean PM2.5 in each GAINS region
Health impacts: annual premature deaths from ambient PM2.5
Exposure distribution: how many people are exposed to different levels of PM2.5?
Source attribution:
  Where does ambient PM in each GAINS region originate from?
  Which sectors are responsible?

## Slide 17: Contributions to state-wise PM2.5 in India

## Slide 18: Contributions to state-wise PM2.5 in India: sectors
Chart: PM2.5 (µg/m³)
| Delhi | West Bengal | Haryana | Uttar Pradesh | Punjab | Jharkhand | Bihar | Rajasthan | Gujarat | Odisha | Chattisgarh | Madhya Pradesh | Maharashtra | Uttarakhand | Assam | Andhra Pradesh* | North East | Goa | Karnataka | Tamil Nadu | Himachal Pradesh | Kerala | Jammu, Kashmir
Natural sources (soil dust, vegetation) | 8.7 | 1.6 | 10.7 | 6.9 | 6.7 | 5.5 | 3.2 | 18.7 | 19.1 | 5.8 | 10.4 | 14 | 11.9 | 4 | 3.7 | 7.5 | 7.7 | 7.8 | 5.5 | 1.5 | 1.9 | 1.2 | 1.8
Secondary PM2.5 (*) | 41.6 | 35.3 | 33 | 31.5 | 27.8 | 29.9 | 29.8 | 14.7 | 13.6 | 23.4 | 19.4 | 15.9 | 16.1 | 15 | 10.1 | 14.1 | 8.4 | 12.1 | 9.3 | 10.1 | 7.5 | 8.9 | 5.4
Coal thermal power plants | 9.1 | 1.1 | 1.3 | 0.9 | 0.7 | 1.2 | 0.6 | 0.4 | 0.8 | 0.6 | 0.8 | 0.5 | 0.9 | 0.3 | 0 | 0.4 | 0.1 | 0.4 | 0.3 | 0.3 | 0.1 | 0.2 | 0.1
Other high stacks | 4.8 | 3.7 | 2 | 2.4 | 2.4 | 4.4 | 1.6 | 0.9 | 1.3 | 2.3 | 2.3 | 1 | 1.4 | 1.1 | 0.4 | 1.2 | 0.3 | 1 | 0.7 | 0.7 | 0.7 | 0.4 | 0.3
Households | 12.8 | 21.1 | 9.8 | 13.1 | 9.3 | 15.2 | 17.9 | 4.2 | 5.2 | 8.3 | 4.9 | 4.9 | 6.2 | 10 | 8.2 | 5.7 | 11.9 | 2.6 | 4.2 | 4.2 | 3.2 | 6.5 | 6.4
Transport | 25.9 | 1.1 | 3.6 | 0.8 | 2.1 | 0.6 | 0.5 | 0.6 | 1.3 | 0.5 | 0.3 | 0.4 | 0.8 | 0.9 | 0.3 | 0.6 | 2 | 1.8 | 0.5 | 1.3 | 0.5 | 2.3 | 0.7
Waste | 13.4 | 1.4 | 0.9 | 1 | 0.9 | 0.6 | 1 | 0.3 | 0.2 | 0.5 | 0.3 | 0.3 | 0.4 | 0.4 | 0.4 | 0.3 | 0.3 | 0.3 | 0.2 | 0.4 | 0.2 | 0.3 | 0.5
Agriculture | 2.2 | 1.3 | 1.3 | 1.4 | 1.5 | 0.8 | 1.2 | 0.8 | 0.7 | 0.7 | 0.8 | 0.8 | 0.9 | 0.7 | 0.7 | 0.4 | 0.6 | 0.4 | 0.3 | 0.2 | 0.3 | 0.2 | 0.3
Other | 8 | 0.8 | 0.6 | 0.7 | 0.5 | 0.4 | 0.8 | 0.2 | 0.3 | 0.3 | 0.2 | 0.2 | 0.3 | 0.3 | 0.3 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.3 | 0.3

## Slide 19: Validation of model results against observations – 2018 Only stations with more than 75% data coverage are considered
India IGP | India – non-IGP States | Bangladesh
Nepal | Pakistan | Sri Lanka