## Slide 1: Calculating ambient PM2.5 and health impacts in GAINS
Gregor Kiesewetter
Pollution Management Group
Energy, Climate and Environment Program
EECCA Workshop, Laxenburg, November 2023

## Slide 2: Principles: PM2.5
PM2.5 is composed of primary PM (PPM) and secondary aerosols
  PPM dispersion
  SO2
  NOx SIA formation: (NH4+)2SO42- , (NH4+)NO3-
  NH3
  VOC SOA formation
  Natural dust, sea salt
  → Pure dispersion models (e.g. Aermod) are not enough, but can be useful at local scale
State of the art atmospheric chemistry-transport models (CTMs) can describe ambient PM2.5 concentrations well, but are time consuming:
  Emission gridding needed every time
  Execution time of the CTM – typically days per 1 year simulation with good resolution
Needed: fast approximation of the full atmospheric model with similar performance
GAINS approach: linearized response model (“atmospheric transfer coefficients”) derived from sensitivity simulations of a full CTM.
Total PM2.5
© US EPA

## Slide 3: How GAINS calculates ambient PM: Transfer coefficients
We use sensitivity simulations of EMEP CTM on 0.3°x0.2° (~22km) to derive transfer coefficients from region → grid . Each sensitivity run changes emissions of pollutant from region by 15%:
For each source region and 5 source pollutants: PPM2.5, SO2, NOx, NH3, VOC
Source region r
Receptor grid i
Pollutant p

## Slide 4: Transfer coefficients
Linear approximation of the full CTM
… 0.3° x 0.2° grid cell
… source pollutant (PPM2.5, NOx, SO2, NH3, VOC)
… source region
… transfer coefficient from emissions of pollutant in region to grid cell
… emissions of pollutant in region
… grid specific constant: natural sources, boundary conditions, non-linearities

## Slide 5: Examples of transfer coefficients
Transfer coefficients have been developed for 60 source regions in GAINS-Europe (50 countries, 10 sea regions)
Example for emissions from Romania in GAINS (0.3⁰x0.2⁰ resolution):
0.3⁰x0.2⁰ or ~22km resolution is good enough for secondary PM but not for primary PM!

## Slide 6: Extension with grid-to-grid tracking of PPM
EMEP CTM can track PPM contributions grid-to-grid (0.1°)
4 different vertical emission “layers” (low-level 1&2, industry, power)
monthly results allow for sector-specific time patterns
Source grid
Receptor grid
Sector specific transfer coefficients

## Slide 7: Extension with grid-to-grid tracking of PPM
EMEP CTM can track PPM contributions grid-to-grid (0.1°)
4 different vertical emission “layers” (low-level 1&2, industry, power)
monthly results allow for sector-specific time patterns
five nested resolutions for source grids: 0.1° / 0.2° / 0.5° / 1° (/ 2°)
Sector specific transfer coefficients (0.1°)
20 grid cells in each direction => Complete domain coverage
Source grid
Receptor grid

## Slide 8: Combination: Sector specific transfer coefficients
GAINS transfer coefficients for secondary aerosols: linear approximation of EMEP CTM
From source regions , source pollutant , to PM2.5 in receptor grid cell :
Grid to grid tracking (“local fraction”) of PPM with EMEP CTM at 0.1⁰, monthly results
=> sectoral transfer coefficients for PPM:
… source region, … source sector, i… receptor grid cell (0.1⁰), … emission grid cell (0.1⁰), …vertical emission layer, …month
… spatial emission distribution pattern
… temporal (monthly) emission share
… grid-to-grid transfer coefficient from to in month for emission layer
So that
(applying relative sectoral contributions also to SO2 and NOx transfer coefficients)

## Slide 9: Sector specific transfer coefficients: PPM
(Coal) power plants
Linear scale
Logarithmic scale
Heavy duty trucks
Heating: rural
A few examples from Romania (~45 sectors in total…)

## Slide 10: Downscaling based on uEMEP
Near-ground emission sources of PPM require higher resolution than 0.1° (10km)
High resolution (100x100m) simulations with the uEMEP model were used to derive PM2.5 exposure increments that allow GAINS to calculate the same population-weighted PM2.5 concentration as if the 100m resolution was used.
This is done for traffic and residential sectors.
Local contribution from traffic, EMEP model (0.1°)
Local contribution from traffic, uEMEP model (100m)

## Slide 11: Ambient PM2.5: Contributions from sectors (2015)
Heating: urban
Heating: rural
Iron & steel industry
Coal power plants
Done for ~40 sectors.

## Slide 12: Ambient PM2.5 concentrations

## Slide 13: Ambient PM2.5 concentrations – validation
Non-EU: Not many stations available…
(WHO DB 2022, AirBase, US Embassies)
Preliminary results!

## Slide 14: PM2.5 and human health
Long-time exposure to PM2.5 increases the risk of cardiovascular and respiratory diseases, and lung cancer
3-5 million cases of premature deaths annually are attributed to it,
making it the most important environmental risk factor for human health.

## Slide 15: Health impact calculations in GAINS
Long-term exposure increases the risk for death from a few diseases: COPD, stroke, IHD, lung cancer, ALRI, diabetes. The relevant factor is called relative risk () and is a function of PM2.5
In Europe, GAINS follows the WHO Europe approach, quantifying all-cause mortality:
Per 10µgm-3, the risk for death increases by 8% (Chen & Hoek, 2020)
(recently updated, previously HRAPIE 2013: 6%/10µgm-3. HRAPIE2 update expected soon)
Needed for the calculations:
  Ambient PM2.5 concentration on relevant resolution (urban background)
  Population data on the same spatial distribution
  Concentration-response relationships
  Baseline mortality data
GAINS
JRC (250m grid)
International literature: WHO,…
UN World Population Prospects

## Slide 16: Basic principle of the calculation
Exposure to PM2.5 increases the risk to die from certain diseases:
… Deaths occurring in a given year under elevated PM2.5 concentrations (“baseline deaths”)
… hypothetical number of deaths under ‘clean’ conditions
…relative risk for this level of PM2.5, derived from epidemiological studies.
GAINS considers all anthropogenic PM2.5 without any lower cut-off (but no natural dust).
To get the additional number of deaths (“premature” or attributable deaths ) caused by PM2.5, we take
Observed (or projected) natural-cause deaths
Population-weighted mean PM2.5

## Slide 17: Years of life lost, Loss of life expectancy
People dying prematurely lose a part of their life expectancy
Years of life lost in a country:
Alternatively to the number of premature deaths in a given year, we can also calculate the loss of life expectancy under constant exposure, using a life table approach. For details see Kiesewetter et al., Environ. Modell. Softw. 2015
Premature deaths
Remaining life expectancy

## Slide 18: Ground-level ozone
Ozone is formed from emissions of NOx and VOC (also CO, CH4 but longer time scales)
Chemistry is non-linear, but the linear approximation is good enough
GAINS calculates SOMO35 as a function of NOx and VOC emissions:
Transfer coefficients are calculated from perturbation simulations of the EMEP CTM at 0.3°×0.2°
source region
pollutant
grid cell

## Slide 19: Ground-level ozone
Ground-level ozone is associated with premature mortality (respiratory diseases)
Mostly a short-term effect during episodes
Exposure indicator: SOMO35 = sum of daily max 8-hour mean O3 >35ppb
time
O3
Highest 8-hour mean within each day
Day 1 Day 2 Day 3
35 ppb
Contributions to SOMO35
Premature deaths: ,

## Slide 20: What GAINS-Europe online currently offers
PM2.5 :
concentration maps
Population-weighted mean PM2.5 in each GAINS region
Blame matrix: How much of the pollution is local, how much is transboundary?
Exposure distribution: how many people are exposed to different levels of PM2.5?
Health impacts:
  Annual premature deaths from ambient PM2.5
  Years of life lost
  Loss of life expectancy
Ozone:
Maps of SOMO35
Premature deaths