## Slide 1: Data import and model documentation
Presented by Laura Warnecke
For the EECCA workshop on the GAINS model

## Slide 2: Data import

## Slide 3: Importing process
Energy models:
IEA: World Energy Outlook data, global
PRIMES: Europe
POTEnCIA: Europe
Other IAMs, e.g.: AIM, MESSAGE, TIMES, GCAM
Agricultural models:
CAPRI: Europe
FAO: FAO Agricultural Outlook model results, global
Regional mapping
Sectoral mapping
Data from external models
Mapping

## Slide 4: Mapping table examples
GAINS Region | GAINS Fuel | GAINS Sector | Ext. model Region | Ext. model Fuel | Ext. model Sector
AUTR_WHOL | HF | TRA_OTS_L | AUNZ | Oil | DOMESNAV
AUTR_WHOL | MD | TRA_OTS_L | AUNZ | Oil | DOMESNAV
AUTR_WHOL | GSL | TRA_OT_INW | AUNZ | Oil | DOMESNAV
AUTR_WHOL | MD | TRA_OT_INW | AUNZ | Oil | DOMESNAV
NZEL_WHOL | HF | TRA_OTS_L | AUNZ | Oil | DOMESNAV
NZEL_WHOL | MD | TRA_OTS_L | AUNZ | Oil | DOMESNAV
NZEL_WHOL | GSL | TRA_OT_INW | AUNZ | Oil | DOMESNAV
NZEL_WHOL | MD | TRA_OT_INW | AUNZ | Oil | DOMESNAV
GAINS Region | GAINS Fuel | GAINS Sector | Ext. model Region | Ext. model Fuel | Ext. model Sector
CHIL_WHOL | GSL | DOM_COM | CHILE | Oil | COMPUB
CHIL_WHOL | GSL | DOM_COM | CHILE | MODBIOLIQ | COMPUB
DISAGGREGATION
AGGREGATION

## Slide 5: Importing process
Energy models:
IEA: World Energy Outlook data, global
PRIMES: Europe
POTEnCIA: Europe
Other IAMs, e.g.: AIM, MESSAGE, TIMES, GCAM
Agricultural models:
CAPRI: Europe
FAO: FAO Agricultural Outlook model results, global
Regional mapping
Sectoral mapping
Data from external models
Mapping
Data in the GAINS format
Import routines, incl. downscaling
Pattern distribution
Seeding
Default ratios
Trend of drivers
Gap filling
Quality checks
Pre-checks, e.g.:
Are all inputs available?
Are there any new categories or changes in the naming?
Post-checks, e.g.:
Do the sums match?
Are there any negative numbers?

## Slide 6: Disaggregation of inputs based on pattern scenario
GAINS Region | GAINS Fuel | GAINS Sector | Pattern scenario number in PJ | Share in % | New input data in PJ, disaggregated to GAINS categories
AUST_WHOL | HF | TRA_OTS_L | 0 | 0 | =0*2=0
AUST_WHOL | MD | TRA_OTS_L | 0 | 0 | =0*2=0
AUST_WHOL | GSL | TRA_OT_INW | 0.1 | 2.17 | =0.0217*2=0.0434
AUST_WHOL | MD | TRA_OT_INW | 1 | 21.74 | =0.2174*2=0.4348
NZEL_WHOL | HF | TRA_OTS_L | 3.5 | 76.09 | =0.7609*2=1.5218
NZEL_WHOL | MD | TRA_OTS_L | 0 | 0 | =0*2=0
NZEL_WHOL | GSL | TRA_OT_INW | 0 | 0 | =0*2=0
NZEL_WHOL | MD | TRA_OT_INW | 0 | 0 | =0*2=0
Sum |  |  | 4.6 PJ | 100% | 2 PJ
Input data
(AUNZ - DOMESNAV - Oil)

## Slide 7: Model documentation

## Slide 8: Help and resources in the online model
User guide/technical documentation
Release notes
Other technical reports
Peer-reviewed papers
Notes: http://gains.iiasa.ac.at/models/gains_models4.html
http://gains.iiasa.ac.at/models/gains_resources.html

## Slide 9: New documentation website
Notes: I:\gueret\GAINS-doc-v1\build\html\start

## Slide 10: Thank you for your time. Feel free to ask questions!