## Slide 1: The GAINS model: power generation EECCA workshop on the GAINS model
Peter Rafaj (rafaj@iiasa.ac.at)
Pollution Management (PM) Group
Energy, Climate and Environment (ECE) Program, IIASA
7 November 2023

## Slide 2
Power generation sector in GAINS - topics
Structure of the sector
Activity projections
Emission factors
Control strategies
Data sources
Online interface

## Slide 3: Defining future GAINS scenarios
Pulling together 3 components:
Activity data
Control strategies
Emission factors
+
+

## Slide 4: Emission calculation principles
i,j,k,m | Country, sector, fuel, abatement technology
Ei | Emissions in country i
A | Activity in a given sector
Ef | “Raw gas” emission factor
effm | Reduction efficiency of the abatement option m
Xm | Implementation rate of the considered abatement measure m

## Slide 5: Fuel Categories in GAINS
Combustible
Coal
  -Hard coal (3 grades)
  -Lignite (2 grades)
Oil products
  -Heavy fuel oil
  -Diesel, Gasoline, LPG
Gaseous fuels
  -Natural gas
  -Derived gases
  -Biogas
Biomass
  -Fuelwood
  -Residuals
Waste
  -Renewable
  -Industrial
Non-Combustible
Hydro
Solar
Wind
Geothermal
Nuclear
Electricity
Heat

## Slide 6: Structure of the electricity and conversion sectors
Power and heat generation
Power plants
Heating plants
CHPs
Existing
New (after y. 2000)
Modern
Large units (>50MWth)
Small units
No-CCS
CCS
DG sets
Engines
Fuel conversion
Conversion processes
Own use
Losses
Refineries
Coking plants
Liquefaction
Boilers
Combustion
Fuel-specific classification
COAL
Subcritical
(Ultra)supercritical
IGCC
GAS
Steam / boilers
Gas turbine
NGCC
BIOMASS
Same as coal
no co-firing

## Slide 7: Activity data sources
International databases:
IEA, EUROSTAT
UN
USGS
Local databases:
National statistics
Provincial statistics
Projections (examples):
PRIMES - Europe
WEO, MESSAGE - Global
Other IAMs

## Slide 8: Activity projections - example

## Slide 9: Visualization in GAINS online - example

## Slide 10: Emission factors for SO2, NOx, and PM
Combustion–related emissions:
  Unabated factors depend on combustion installation, fuel type and fuel quality
    Either calculated based on fuel quality parameters
    Or based on measurements for typical installations
  Abated factors depend on controls
    Efficiency of abatement technology
    Application rate of technologies / measures (time depended)

## Slide 11: Emission factors calculation
ef | “Raw gas” emission factor
sc | Sulphur content of a fuel
hv | Lower heating value
sr | Sulphur retention in ash
ef | “Raw gas” emission factor
ac | Ash content of a fuel
hv | Lower heating value
Ar | Ash retention in boilers
SO2
PM

## Slide 12: Visualization in GAINS online - example

## Slide 13: Emission control options for SO2
Use of low sulfur coal 0.6% S
Use of low sulfur heavy fuel oil 0.6% S
Use of low sulfur diesel (3 stages) 0.2 - 0.001% S
Use of low sulfur gasoline 0.001% S
In- furnace control (limestone inj.) 60%
Flue gas desulfurization 85 - 95%
Wet FGD 90%
Advanced flue gas desulfurization 98%

## Slide 14: Emission control options for NOx
For stationary sources
  Combustion modifications 20 - 65 %
  SNCR 70 %
  SCR 80 %
  CM + SCR combined
For small sources (engines)
  Euro equivalents 30 – 90 %

## Slide 15: Emission control options for PM
For stationary sources
  Cyclones 30%
  Wet scrubbers 50 – 93%
  ESPs (1 and 2 fields) 93 – 96%
  ESP3 and fabric filters 99 – 99.5%
  Good practices
For small sources (engines)
  Same as for NOx

## Slide 16: Control strategy in emission scenarios
  It is a way of defining legislation in GAINS
  Includes a list of all measures and contains non-zero values for implemented measures in the defined policy
  The values reflect the level of application as a percentage of total activity in the sector
  For each technology the value is between 0% and 100%
  % is always relative to activity
  For power plants activity means fuel input

## Slide 17: Application rates of abatement measures: % of activity

## Slide 18: How do I calculate a control strategy? Example: Coal-fired power plants
500 MWel
250 MWel
STEP 1: Start with capacities: Total = 800 MWel
50 MWel

## Slide 19: How do I calculate a control strategy?
500 MWel
250 MWel
50 MWel
Step 2: Calculate fuel input per year, using
    Operating hours per year
    Conversion efficiency
4,000 hours/yr, 35% efficiency
2,000 hours/yr, 30% efficiency
6,000 hours/yr, 32% efficiency
20.6 PJ/yr = 69%
6.0 PJ/yr = 20%
3.4PJ/yr = 11%

## Slide 20: How do I calculate a control strategy?
Step 3: Determine control technology in operation
20.6 PJ/yr = 69%
6.0 PJ/yr = 20%
3.4PJ/yr = 11%
e.g. flue gas desulfurization
e.g. lime stone injection
e.g. no control

## Slide 21: How do I calculate a control strategy?
Apply control strategy here

## Slide 22: How do I calculate a control strategy?
Flue gas desulphurization = 69%
Lime stone injection = 20%
No control = 11%

## Slide 23: What is the origin of GAINS data? [emission factors and ef parameters, reduction efficiencies and costs of abatement]
Guidebooks (EEA/EMEP, AP-42, BUWAL)
UNECE Expert Groups
National submissions (consultations)
International databases, e.g., CEPMEIP
Industrial associations
Peer-reviewed literature
Grey literature
Own expertise

## Slide 24
    Comparison to legislation

## Slide 25
    Mapping and calibration of control strategies
130
127

## Slide 26: Visualization in GAINS online - example

## Slide 27
rafaj@iiasa.ac.at