## Slide 1: GAINS – Calculations of air pollutant control costs
Peter Rafaj (rafaj@iiasa.ac.at)
Pollution Management (PM) Group
Energy, Climate and Environment (ECE) Program, IIASA
Laxenburg November 2023

## Slide 2: Application rates of abatement measures: % of capacity / activity

## Slide 3: Cost concept used
All costs are in (economic) real terms (2005)
Societal costs:
  Standard discount rate: 4 percent p.a.
  Taxes not included
  Transaction & training costs not included
Feedback on economy not included (small)
Technology costs
  Non-technical measures not included
  Investment, Operating and Maintenance costs, Labour cost, Energy costs, etc.
  Are constant over time

## Slide 4: Calculations principles
GAINS calculates annual costs of emission control technologies consisting of:
  Investment costs (annualized)
  Fixed O+M costs
  Variable O+M costs
C = Iann + OMfix + OMvar

## Slide 5: Cost information in the literature Example: Flue gas desulphurization (FGD)
Scrubber type | Unit size MW | Capital Cost $/kW | O&M cost - fix $/kW | O&M cost - var $/MWh
Wet | >400 | 100-250 | 2-8 | 0.5-2
Wet | <400 | 250-1500 | 8-20 | 0.5-2
Spray dry | >400 | 40-150 | 4-10 | 0.5-2
Spray dry | <400 | 150-1500 | 10-300 | 0.5-2

## Slide 6: Costs are country- and technology-specific
Technology-specific factors:
Investments, fixed O+M
Demand for labour, energy, by-products
Lifetime of equipment
Removal efficiency
Country-specific factors:
Installation size, plant factors
Prices for labour, energy, by-products, etc.
Applicability

## Slide 7: Units used
Costs per unit of activity
  E.g. MEuro per PJ
Costs per ton of pollutant removed
  E.g. Euro per ton of PM
“per year” is always implicit

## Slide 8: Marginal costs
Marginal cost – extra cost for an additional measure related to extra abatement of that measure
Where:

## Slide 9: An example marginal cost curve for SO2