## Slide 1: The Greenhouse Gas and Air Pollution Interactions and Synergies (GAINS) model: Solid waste – Indo Gangetic Plain Adriana Gómez-Sanabria
October 2020

## Slide 2
Identify emission sources
Current Policies - commitments regarding waste management but also emission reductions from waste
’Calibration’ historical years
Suggest technical and behavioural measures
Data Sources
Inventories: identify waste generation, composition, management
Projections

## Slide 3
Country/region
Socio-economic drivers
(i.e. Population growth, GDP per capita, Urbanization rate, value added, etc.)
Behavioral Policies (e.g. Waste reduction - less water consumption)
Waste and wastewater treatment facilities
Landfill
Incinerator
Anaerobic digester
Composting facilities
Recycling facilities
Centralized wastewater treatment plants
GHGs, water and air pollution
Technical measures: Development and efficiency improvement
Unmanaged
Waste and wastewater sector in GAINS
Industrial wastewater
Domestic wastewater
Industrial solid waste
Municipal solid waste
Waste and wastewater generation
Decentralized wastewater treatment
Clean Environment
(e.g. reduction of pollutants in wastewater)
Circularity of resources
(e.g. Prolonging lifetime of materials, energy provision)
Emissions and environmental impacts

## Slide 4: Waste management technologies

## Slide 5: MSW generation - projections
Activity drivers: GDP per capita – Urbanization rate
Projections of Total MSW generation based on the elasticity to GDP/cap and urbanization rate for different income groups. Future growth in food waste generation suppressed at higher income levels due to its inferior goods nature.
Waste fraction | ε Income
Food waste | 0.43

## Slide 6: MSW generation - Composition

## Slide 7
India MSW generation and treatment - 2015
241
122
119
25
4
3
26
35
29
76
44
Values in Mton
Chart: Rural
| Food | Glass | Metal | Other | Paper | Plastic | Textile | Wood
sh | 53.4703 | 1.9793 | 1.7908 | 20.9877 | 5.3723 | 3.6758 | 3.2988 | 9.4251
Chart: Urban
| Food | Glass | Metal | Other | Paper | Plastic | Textile | Wood
sh | 49.4703 | 1.9793 | 1.7908 | 24.9877 | 5.3723 | 3.6758 | 3.2988 | 9.4251

## Slide 8
Municipal Solid Waste Generation
Chart: Municipal solid waste
| India | IGP
2015 | 241.3298 | 104.279
2018 | 265.8225 | 114.4505

## Slide 9: MSW up to 2050
Current IGP 104 Mt  242 Mt in 2050
IGP 43% of MSW generates in India
Chart: [Mt]
| 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
West Benegal | 28.2341 | 34.2024 | 41.5089 | 48.6347 | 55.7229 | 59.9473 | 63.5718 | 66.5369
Bihar | 20.7544 | 24.4858 | 28.8879 | 32.7424 | 36.3246 | 39.3326 | 41.6175 | 43.1085
Delhi | 4.4445 | 5.4845 | 6.8075 | 8.1527 | 9.5413 | 10.9867 | 12.4262 | 13.8157
Haryana | 5.5464 | 6.6624 | 8.029 | 9.4391 | 10.3484 | 11.1788 | 11.9067 | 12.5164
Punjab | 6.6049 | 8.0251 | 9.7885 | 11.6052 | 12.807 | 13.93 | 14.935 | 15.8016
Uttar Pradesh | 38.6947 | 45.7617 | 54.2741 | 63.029 | 71.1741 | 78.5839 | 84.9278 | 89.9522
#REF! | 1
IGP | 104.279 | 124.622 | 149.2959 | 173.6031 | 195.9183 | 213.9594 | 229.3851 | 241.7313

## Slide 10
Municipal Solid Waste Collection Rates
Most of the waste collected is mixed. Not waste segregation at source.

## Slide 11
Municipal solid waste treatment 2015
~ 29% of the total waste generated is openly burnt
~31% is scattered waste (with high probability of contaminating water courses)
Although urban areas have high collection rates, ~23% end up in dumpsites
Informal recycling
Waste to energy technologies are limited and also methane recovery from landfills
Composting plays a significant role in rural areas
Chart: Indo-Gangetic Plain
| Total | Rural | Urban
Anaerobic Digestion | 0 | 0 | 0
Composting | 0.11216 | 0.17207 | 0.016104
Recycling | 0.015159 | 0 | 0.039464
High quality incineration | 0 | 0 | 0
Sanitary landfill gas flaring/recovery and use | 0.017953 | 0 | 0.046739
Landfill | 0.11484 | 0.0038205 | 0.29284
Dumpsite | 0.14311 | 0.089308 | 0.22939
Open burning collected waste | 0.086326 | 0.017364 | 0.1969
Open burning uncollected waste | 0.2024 | 0.27977 | 0.078348
Scattered | 0.30805 | 0.43767 | 0.10022

## Slide 12: Emissions PM2.5
Currently PM2.5 emissions from municipal solid waste account for ~10% of the total PM2.5 emissions in India
IGP accounts for 40% of PM2.5 emissions from municipal solid waste
IGP 2015 - 257 kt PM2.5 – Projected to grow to 585 kt by 2050
Chart: [Kt]
| 2015 | 2018 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
West Benegal | 65.8722 | 71.9075 | 77.9428 | 92.1004 | 104.7456 | 116.1767 | 119.7029 | 123.7663 | 125.085
Bihar | 50.0676 | 54.7399 | 59.4123 | 70.5688 | 80.6084 | 90.2143 | 97.4803 | 105.851 | 110.9073
Delhi | 4.889 | 5.4573 | 6.0256 | 7.4701 | 8.9355 | 10.4454 | 12.061 | 13.5593 | 15.0566
Haryana | 14.9133 | 16.4839 | 18.0546 | 21.9446 | 26.0344 | 28.8137 | 31.0752 | 33.8661 | 35.9365
Punjab | 18.0564 | 20.0806 | 22.1048 | 27.1822 | 32.505 | 36.1892 | 39.2866 | 43.0657 | 45.9659
Uttar Pradesh | 103.0208 | 112.7535 | 122.4862 | 146.1458 | 170.8526 | 194.3236 | 213.944 | 236.3338 | 252.4661
IGP | 256.8193 | 281.4228 | 306.0263 | 365.4119 | 423.6816 | 476.1629 | 513.5501 | 556.4422 | 585.4174

## Slide 13: Emissions PM2.5
Currently PM2.5 emissions from municipal solid waste account for ~10% of the total PM2.5 emissions in India
Projected to be 19% in 2050 under the current conditions
Chart: [kt]
| 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Power and heating plants | 464.2 | 451.4 | 244.5 | 135.7 | 144.9 | 134.8 | 131.7 | 126.5
Fuel conversion | 0.5 | 27.3 | 27.9 | 28.7 | 29.4 | 29.9 | 30.1 | 30.1
Residential combustion | 2785.4 | 2273.9 | 1991.3 | 1769.1 | 1593.7 | 1420.9 | 1257.7 | 1107.1
Industrial combustion | 702.4 | 494.3 | 602.4 | 706.1 | 803.2 | 879.1 | 949.2 | 990.9
Industrial processes | 803.6 | 935.4 | 1301.4 | 1728.6 | 2229.3 | 2665.7 | 3046.7 | 3325
Fuel production & distribution | 3.8 | 4.6 | 5.8 | 7 | 8.1 | 9.2 | 9.9 | 10.4
Light duty vehicles | 52.5 | 56.2 | 54.8 | 46.9 | 44.6 | 47.3 | 50.3 | 52.7
Heavy duty vehicles-diesel | 373.9 | 266.8 | 259.4 | 244.1 | 230.6 | 224.7 | 216.3 | 232.3
Non-road machinery | 58.2 | 62.1 | 63.4 | 62.3 | 66.7 | 70.2 | 74.1 | 75.2
Agriculture | 530.8 | 520.7 | 510.5 | 500.4 | 503.1 | 505.8 | 508.4 | 511
Waste | 636.7357 | 769.3105 | 932.55 | 1097.1755 | 1247.0992 | 1360.3532 | 1490.5739 | 1586.0601
Other | 235.6643 | 250.7895 | 265.05 | 278.7245 | 288.0008 | 295.2468 | 300.3261 | 303.8399

## Slide 14: Sectoral contribution PM2.5
Notes: Secondary PM it is created by secondary formation from precursor emissions such as sulfur dioxide (SO2), nitrogen oxides (NOx), volatile organic compounds (VOCs) and ammonia (NH3). Items 1 and 2 are generally known as primary emissions of PM2.5. Secondary formation occurs due to chemical reaction in the atmosphere generally downwind some distance from the original emission source. Efforts to determine the contribution of each of these PM2.5 emission mechanisms has shown a great deal of variability, as seen from an examination of current literature.

## Slide 15
Notes: Secondary PM it is created by secondary formation from precursor emissions such as sulfur dioxide (SO2), nitrogen oxides (NOx), volatile organic compounds (VOCs) and ammonia (NH3). Items 1 and 2 are generally known as primary emissions of PM2.5. Secondary formation occurs due to chemical reaction in the atmosphere generally downwind some distance from the original emission source. Efforts to determine the contribution of each of these PM2.5 emission mechanisms has shown a great deal of variability, as seen from an examination of current literature.

## Slide 16: Questions /discussion
Activity data can still be refined
Not really information on quantities of municipal solid waste open burnt…..data comparison difficult
Information on policy implementation is missing …..current state of policy implementation
………………
Hands on….….

## Slide 17: GAINS IGP
Activity data:
Total municipal solid waste generation
Municipal solid waste generated in urban areas: MSW_URB
Municipal solid waste generated in rural areas: MSW_RUR
Composition of waste
8 fractions  sum of the fraction should be 1 for each group.
MSW_URB_FOOD
MSW_URB_GLA
MSW_URB_MET
MSW_URB_OTH
MSW_URB_PAP
MSW_URB_PLA
MSW_URB_TEX
MSW_URB_WOOD
MSW_RUR_FOOD
MSW_RUR_GLA
MSW_RUR_MET
MSW_RUR_OTH
MSW_RUR_PAP
MSW_RUR_PLA
MSW_RUR_TEX
MSW_RUR_WOOD